## Slide 1: Parallel Interface –high level view

## Slide 2: Solution Space for Parallel I/F PHY Standardization
Medium / Bump map
  Interposer/EMIB
  Organic Substrate
Channel Signal Definition
  2 clocks (diff. pair) per 32 data plus TBD aux pins
  2 clocks (diff. pair) per 16 data plus TBD aux pins
Electricals – Select/Leverage from JEDEC compliant IOs
  HBM 2/2E, 3
  LP-DDR4, LP-DDR5
  DDR4, DDR5
  GDDRx ;
  Optimized derivative of one of the above
  What is required voltages? Recommended voltages

## Slide 3: Simplifying the Solution Space for Parallel PHY
Medium / Bump map
  Interposer/EMIB
  Organic Substrate
Channel Signal Definition
  2 clocks (diff. pair) per 32 data plus TBD auxiliary pins
  2 clocks (diff. pair) per 16 data plus TBD auxiliary pins
Electricals –
  HBM 2/2E, 3
  LP-DDR4, LP-DDR5
  DDR4, DDR5
  GDDRx ;
  Optimized derivative of one of the above
  What is required voltages? Recommended voltages
Interposer/EMIB/InFO/HDFO &
1 diff clock pair per 32 &
HBM 2/2E, 3 Electricals
Organic substrate &
1 diff clock pair per 16 &
Questions –
Required inter-operation voltage
Type of termination for the terminated case

## Slide 4: Benefits of new proposal:
We don’t see chiplets in the AIB EMIB/interposer world can be reused for organic substrate so BoW choice of 0.9V doesn’t benefits interoperability. BoW and AIB signals definition are different as well.
We believe BoW spec with following characteristics can greatly accelerate chiplets ecosystem buildup:
  Available IP and proveness, Ease of design, Low BOM Cost, Device ecosystem and Test infrastructure
  Preferably, Dual- or Multi-role enables industry support without “dedicated cost” to it if the interface is unused
    Especially important in early phase of market adoption, often “chicken-and-egg” situation
  Roadmap to both higher data rates and lower energy/bits to optimize for different use cases
 | BoW (with 0.9V I/O) | BoW using Industry-standard I/Os
Industry-standard I/Os | - | adopt LP-DDRx, DDRx standards I/O
Optimized for organic substrate | Goal is to support both organic and interposer | Y
Roadmap to lower energy/bit Roadmap to higher max data rates | - | Y LP5 VDDQ 0.3V (unterm): 1-4Gbps (short ch) LP5 VDDQ 0.5V required (term): 4-16Gbps (short ch)
Ease of design / Lower design cost | - | Y I/O IPs readily available from multi-vendors
Dual-role possible | - | Y (Chiplets and Memory)
Lower BOM cost | N (need extra 0.9V rail, dedicated usage) | Y (standard rail, dual-role flexibility)
Device availability / maturity timeline |  | Y (/ soon for latest standards)
Test infrastructure |  | Readily available, multi-vendors